; Contact: ; Ron Kiino Ariel Gavilan ; . Fiat 500 Abarth and Abarth Cabrio Offer Automatic Transmission Option for 2015 Six-speed automatic transmission available as an option to five-speed manual transmission on 2015 Fiat 500 Abarth and Abarth Cabrio Specially tuned automatic transmission maintains high-performance legacy of Abarth models while delivering accessible performance to more customers 2015 Fiat 500 Turbo will also offer an optional automatic transmission April 7, 2014, Auburn Hills, Mich. - The high-performance 2015 Fiat 500 Abarth and Abarth Cabrio, to be showcased at the 2014 New York International Auto Show, will be available with an optional six-speed automatic transmission, helping to broaden the customer base for the high-performance version of the Fiat 500. “Adding an optional automatic transmission makes the Abarth and Abarth Cabrio accessible to an entirely new group of customers who want to enjoy the thrilling driving experience of the Fiat 500 Abarth with the convenience of an automatic gearbox,” said Jason Stoicevich, Head of FIAT Brand for North America, Chrysler Group LLC. To ensure the 2015 Fiat 500 Abarth and Abarth Cabrio remain true to their high-performance and track-ready heritage, the six-speed automatic transmission – Aisin AW6F25 six-speed – has been reinforced with more clutch plates and a more robust heat treatment to allow for higher torque capability. The Sport mode calibration allows for an even more engaged driving experience with special features such as fuel-cut upshifts, rev-matching downshifts, brake-assist downshifts, corner gear hold and fast-off gear hold, as well as a more aggressive pedal map. Both the automatic and manual transmission options for the 2015 Fiat Abarth and Abarth Cabrio will be paired with the 1.4-liter MultiAir Turbo engine. Both Abarth models will continue to include the segment-exclusive Abarth Track Experience, which allows Fiat 500 Abarth drivers to learn how to maximize their driving skills with a full day of professional driving instruction. Fiat 500 Turbo The Fiat 500 Turbo was introduced in 2012 for driving enthusiasts who wanted the Italian style of the Fiat 500 with more power and performance for their daily drive. For the 2015 model year, the Fiat 500 Turbo will also offer the Aisin AW6F25 six-speed automatic transmission as an option to pair with the 1.4-liter MultiAir Turbo engine. As one of the more affordable turbocharged vehicles available, the Fiat 500 Turbo amplifies the Cinquecento’s power, performance and personalization levels while keeping the character of the iconic Fiat 500. “When it was launched two years ago, the Fiat 500 Turbo hit the sweet spot between the regular Fiat 500 and the high-performance Fiat 500 Abarth,” said Stoicevich. “The availability of the automatic transmission now makes this sweet spot even sweeter, by expanding the Turbo’s appeal, particularly among young buyers who can now buy one of the most affordable turbocharged cars in the market with the convenience of an automatic transmission.” The Fiat 500 Turbo continues to offer a distinctive look, with an aggressively styled front fascia, bolder side skirts and unique 16-inch aluminum wheels. At the rear, a liftgate-mounted spoiler extends the roofline, while a black-accented rear diffuser optimizes airflow. In addition to the optional automatic transmission offering for the 2015 Fiat 500 Abarth and Turbo models, the entire Fiat 500 lineup will receive interior updates for 2015, including an innovative instrument panel with a 7-inch high-definition display to help drivers easily monitor vehicle information. The 2015 Fiat 500 lineup will arrive at Fiat studios nationwide in July 2014. FIAT Brand FIAT brand celebrates 125 years as an automaker and some things haven’t changed. Iconic Italian design and refinement, plus a fun-to-drive factor, come standard with every Fiat. In early 2024, FIAT brand will launch the Fiat 500e, the first Stellantis retail battery-electric vehicle offering in North America and the best-selling city EV in Europe. FIAT is part of the portfolio of brands offered by leading global automaker and mobility provider Stellantis. For more information regarding Stellantis (NYSE: STLA), please visit www.stellantis.com Follow FIAT and company news and video on: Company blog: http://blog.stellantisnorthamerica.com Media website: http://media.stellantisnorthamerica.com Fiat brand: www.fiatusa.com Fiat blog: blog.fiatusa.com Facebook: www.facebook.com/fiatusa Instagram: www.instagram.com/fiatusa Twitter: www.twitter.com/fiatusa or @StellantisNA YouTube: www.youtube.com/fiatusa or https://www.youtube.com/StellantisNA ; .

-###- Additional information and news from Stellantis are available at https://media.stellantisnorthamerica.com.